## Slide 1: Intra-Operative Neurophysiologic Monitoring
Mark M. Stecker MD, PhD, FASNM, DABNM
President ASNM 2006-2007
Department of Neurology
Geisinger Medical Center
Danville, Pa 17822

## Slide 2: What is Intra-Operative Neurophysiologic Monitoring (IOM)?
Intra-Operative Neurophysiologic Monitoring:
  The Goal: Prevent Damage to the Nervous System During Surgery.
  The Problem: The Patient is Anesthetized during Surgery and so it is not Possible to Perform the Standard Neurologic Examination.
  The Solution: Monitor Electrical Studies that depend on the Integrity of Neural Structures.

## Slide 3
IOM As An Extension of The Neurologic Examination
Neurological Exam
  Cognitive
  Motor
  Sensory
  Reflexes
IOM
  Can Test Only When Awake
    Indirect monitoring of Cortical Function
      EEG
      Cerebral Blood Flow
  Multiple Modalities
    MEP (motor evoked potentials)
    CMAP(compound motor evoked potentials)
  Sensory EP’s
    SSEP
    BAER
    Nerve Action Potential
  H Reflexes

## Slide 4
Specific Purposes of IOM
Issue warning to the surgical team when there is significant evidence of impending injury to important neural structures.
  Also provide SEVERITY of warning!!!!!
Provide information to help guide the surgical resection of lesions, placement of electrodes, or placement of lesions.
  Also provide level of CONFIDENCE information!!!!
Training
  If there are negative outcomes of surgical procedures, correlation of warning with surgical events helps surgeon understand which specific maneuvers place the patient at highest risk and modifies technique in the future to avoid them.

## Slide 5: History of IOM
1920’s-Electrical Stimulation for Localization (Foerster)
  Awake Patients
1930-1950-EEG Recording from Cortex to Localize Epilepsy (Foerster, Jasper, Penfield)
  Awake Patients
1977---First Report of IOM during spine surgery (Nash and Brown).
  First Studies with Patients under General Anesthesia
1980’s--Applications of Evoked Potentials to Brain, Brainstem, Extracranial EMG
1986—Application of Transcranial Doppler in the OR
1994—EMG Monitoring For Pedicle Screw Placement
2002---FDA Approval for Motor Evoked Potentials (MEP)

## Slide 6: Modalities Monitored-I
EEG (Electroencephalogram)
  Spontaneous Electrical Activity in the Brain
    Sensitive to injury to large areas of brain.
Sensory Evoked Potentials
  Responses to Stimulation
  Visual Evoked Potentials
  Auditory Evoked Potentials
  Upper and Lower Extremity Evoked Potentials
    Sensitive to injury on specific pathways

## Slide 7: Modalities Monitored-II
Motor Evoked Responses
  Response to Stimulation of the Motor Areas of the Brain
EMG
  Spontaneous Electrical Activity
  Increases Briefly with Nerve Injury
Nerve Conduction Studies
  Integrity of Peripheral Nerves

## Slide 8: Modalities Monitored-III
Transcranial Doppler
  Measures Blood Velocity in Major Cerebral Vessels.
Near Infrared Spectroscopy
  Measurements of Cerebral Oxygenation

## Slide 9: Properties of Monitoring Modalities-I
Property | SSEP | BAER | EEG | Cortical EEG | MEP | TCD | NIR
Sensitive to Cortical Injury | ++ (Only Parietal) | - | +++ | ++++ (Local) | - | - | -
Sensitive to Subcortical Injury | ++ (Only Thalamus) | - | +/- | +/- | ++ | - | -
Sensitive to Brainstem Injury | ++ | ++ | - | - | ++ | - | -
Sensitive to Ischemia | ++ | ++ | +++ | ++++ | +++ (Esp Cord) | +++ | +++
Sensitive to Seizures | - | - | +++ | ++++ | - | - | -

## Slide 10
Properties of Monitoring Modalities-II
Property | SSEP | BAER | EEG | Cortical EEG | MEP | TCD | NIR
Sensitive to Narcotics | - | - | ++ | ++ | +/- | - | -
Sensitive to Halogenated Anesthetics | ++ | - | +++ | +++ | +++ | - | -
Sensitive to Propofol | + | - | +++ | +++ | + | - | -
Difficult to Setup | ++ | + | ++++ | + | +++ | + | -
Difficult to Interpret | + | + | +++ | ++++ | + | + | ++
Rate of Technical Failure | + | ++ | + | ++ | ++ | ++ | +

## Slide 11
Choice of Monitoring Modality Dependson Structure at Risk and Mechanism of Injury
Structure at Risk
  Peripheral Nerve
    EMG
    Nerve Conduction Study
    SSEP
  Spinal Cord
    MEP
    SSEP
  Brainstem
    BAER
    SSEP
    MEP
    Cranial Nerve EMG
  Brain
    EEG, SSEP
    TCD, NIRS
Mechanism of Injury
  Vascular
    Hypotension
    Vascular Occlusion
  Mechanical
    Compression
    Stretch
  Anatomic Misidentification
    Is the Structure Seen By the Surgeon What it Appears to Be?

## Slide 12: A Very Simple Example “Getting the Data”
Monitoring Upper Extremity SSEP
During Surgery to Repair a Basilar Aneurysm
It’s NOT Easy!!!!!!!!!

## Slide 13: Upper Extremity SEP’s
Erb’s Point---Brachial Plexus
N11------------Root Entry Zone
N13------------Cervico-Medullary Junction
N18------------Ponto-Mesencephalic Junction
N20-------------Thalamus
P22--------------Cortex

## Slide 16
Baseline

## Slide 17
With Aneurysm Clipping

## Slide 18: Using the Data

## Slide 19
Interpreting Changes In IOM-I
The Key
  Although IOM results reveal some information about the nervous system, the relationship between changes in monitored variables and clinical outcome is NOT obvious and NOT fully explored.
The Problem
  Changes in many physiologic variables such as temperature, blood pressure, anesthesia, position, changes in recording or stimulating electrodes ALL affect IOM.
  To date it has not been possible to automatically control for the effects of all of these variables.
  No reliable large scale studies to define specificity and sensitivity of warnings provided by IOM.

## Slide 20
Interpreting Changes In IOM-II
The Solution
  Consensus of expert opinion regarding warning criteria.
    50% decrease in amplitude
    10% increase in latency
  Warnings should be issued based on detailed knowledge of the surgical events.
    A change happening when the surgeon is working on the skin is less significant than when the surgeon is working directly on the spinal cord.
  Warnings are more significant when there is evidence from multiple different tests that there is a potential problem.

## Slide 21: Interpreting Changes In IOM-III
The key to providing appropriate interpretations of significant warnings is:
  Training
  Experience
  Education
  Cooperation between Surgery, Anesthesia, Monitoring Teams
Technicians are to provide waveform descriptions NOT interpretations
Neurophysiologist or Neurosurgeon is to provide interpretations.

## Slide 22: Differences Between IOM and Diagnostic Procedures-I
Although IOM uses standard diagnostic procedures, the practice of IOM is VERY DIFFERENT than that of diagnostic neurophysiology:
  Results
    IOM---must be immediate (<3 minutes)
    Extra-Operative Diagnostics—24 hours
  Interpretation
    IOM—Criteria are qualitative only based on consensus of experts not formal studies.
    Extra-Operative Diagnostic----Formal criteria exist for interpretation with known sensitivity and specificity.

## Slide 23
Differences Between IOM and Diagnostic Procedures-II
Other differences between IOM and Extra-Operative Diagnostics
  Performance
    IOM---Testing is performed continuously and each test is compared to results from prior test and baseline.
    Extra-Operative Diagnostics—Test performed once.
  Multiple Tests
    IOM—Performed simultaneously in order to confirm diagnosis.
    Extra-Operative Diagnostic----Performed serially and can be interpreted separately.

## Slide 24
Differences Between IOM and Diagnostic Procedures-III
Other differences between IOM and Extra-Operative Diagnostics
  Supervision
    IOM---Requires personal supervision either by physical presence in the OR or by real time remote monitoring.
    Extra-Operative Diagnostics—General or direct supervision is appropriate in most cases.

## Slide 25: Summary
IOM is an important technique for providing improved outcomes after complex surgical procedures.
Although IOM uses various diagnostic modalities, it is very different requiring different staffing and interpretation.
It is important to perform outcome studies
  determine how often IOM is used.
  determine which cases need monitoring
  determine optimal criteria for interpreting study results.