## Slide 1: Implantable Hemodynamic Monitor (IHM)
Jamie B. Conti, M.D.
Associate Professor of Medicine Director, Clinical Cardiac Electrophysiology Training Program Director Clinical Cardiac Electrophysiology and Cardiovascular Diseases University of Florida

## Slide 2: IHM Overview
Used in management of severe heart failure
Procedure involves implanted sensor and implanted monitor
Continuous right heart pressures are collected for download and analysis to guide treatment decisions

## Slide 3: Hemodynamic goals for advanced HF patients
Increased Intracardiac Pressure
HF Symptoms
NYHA Class
Most symptoms in advanced heart failure result from congestion
To relieve these symptoms requires reduction of elevated filling pressures.
Diabetes and renal dysfunction are frequent as co-morbidities and further complicate management and follow-up of these patients
HF patient outcome

## Slide 4: Intracardiac Pressure
Increased intracardiac pressure = increased volume status
Symptoms of increased volume status
  Congestion in lungs
  Pulmonary edema

## Slide 5
Management of volume status is an established cornerstone of heart failure management.
Role of Intracardiac Pressures
RH Pressures
• Pulse pressure
• RV Systolic and diastolic pressure
• Estimated pulmonary artery diastolic pressure (ePAD)
• Heart rate & activity
• RV dP/dt (+ / -)
• Pre-ejection interval (PEI)
• Systolic time interval (STI)
Most symptoms in advanced heart failure result from congestion
To relieve these symptoms requires reduction of elevated filling pressures / volume

## Slide 6: Challenges of HF Management
In the treatment of heart failure, measurement of right heart pressures provides key information
Yet, regardless of practitioner skill, it is very difficult to accurately predict and manage

## Slide 7: Challenges of HF Management
Requires frequent exam and monitoring to adjust medication and maintain stable fluid status
High pressures are not always detected by clinical assessment
Weight and edema are not always reliable
Despite optimal management readmission rates are over 40% within 6 months of discharge

## Slide 8: Monitoring via Cardiac Cath
Conventionally, pressures are monitored by right heart cardiac catheterization
Multiple limitations to this method:
  Provides data only for a single point in time
  Must be performed repetitively, exposing patients to repeated risks, additional costs
  Evaluates patients in controlled conditions (supine, at rest, in hospital)

## Slide 9: Monitoring via IHM
Benefits include:
  Single invasive procedure
  Evaluates patients under normal conditions (while they are ambulatory and pursuing daily activities of living)
  Provides continuous pressure data, enabling physician to manage patient care on an on-going basis
IHM provides alternative for monitoring of intracardiac pressures

## Slide 10: Specialized Systems
Two implanted components:
  Pressure sensor “lead”
  - inserted transvenously
  - rests at RVOT
  - takes continuous measurements and transmits to monitor
  Monitor
  - implanted in subcutaneous pocket
  - stores pressure readings
Chronicle® IHM

## Slide 11
Data Analysis
IHM
Home Station
Clinician review
Secure Network
Data stored in monitor is transmitted by patient via a remote station to a secure database
Clinician accesses database to retrieve data
Clinician analyzes data together with other patient-specific data (symptoms, daily weights, physical signs) to guide treatment decisions.
Notes: The Chronicle Implanted Hemodynamic Monitor System comprises an implanted pacemaker size monitor and a pressure sensing lead placed in the right ventricular outflow tract. Intracardiac pressures are measured continuously and stored in the device. Information from the device is then intermittently transmitted by the patient via a remote monitor, from their home (or from the clinic or hospital setting) to a secure website accessible by treating clinicians. Information from the Chronicle system together with other patient-specific data (as available, such as symptoms, daily weights, physical signs) are used to guide treatment decisions. Chronicle has an implantable pressure sensor, which provides access to hemodynamic information that can be used to optimally tailor medical therapy to the individual patient with heart failure. The device is similar to a basic single chamber pacemaker in size and implant requirements. It has one lead with special sensors that reside within the heart (placed in the right outflow tract). The sensor continuously observes and records objective physiologic measurements of hemodynamic right ventricular (RV) pressures, heart rate and activity for patients with heart failure. This information can be retrieved via telemetry for viewing by the clinician one of two ways: while the patient is in the clinic, via the programmer, or remotely from home or any location, via Medtronic’s CareLink.

## Slide 12: Overview of Procedure
Attain venous access
Place the pressure sensor lead in the right ventricular outflow tract
Create pocket for IHM
Verify fixation and placement of the lead captures pressure
Adjust the slack on the lead, secure the lead, place device and close pocket

## Slide 13: Differentiating IHM from Other Implantable Cardiac Devices
Pacemakers and ICDs
  Therapeutic devices to treat arrhythmias
  Leads are tipped with electrodes which send out electrical stimulation
Implanted Loop Recorders
  Monitoring devices but for heart rhythms (EKG), not pressures, usually to diagnose syncope
  Implanted in subcutaneous pocket but no leads

## Slide 14: Differentiating IHM from Other Types of Circulatory Monitoring
Circulatory Monitoring
Temporary
External, generally catheter based
Point in time
Provide monitoring
Not conducive outside hospital setting
IHM
Permanent
Internal with implanted sensor and device
Chronic / continuous
Provides pressure data to guide patient care
Ambulatory

## Slide 15: FDA Status of IHM
At this time, Chronicle is an Investigational Device, limited by United States Law to investigational use only
Recent subject of major clinical study (COMPASS-HF)
Study completed and results presented in Spring 2005
All data have been submitted to the FDA for scientific and regulatory review (PMA)
FDA approval for the first IHM device is expected in Spring 2006

## Slide 16: Summary
Appropriate medical therapy for patients with heart failure depends on accurate detection of volume status
IHM systems continuously measure ambulatory right heart hemodynamics to guide care and reduce hospitalizations
IHM systems are distinct from other implanted cardiac devices and other forms of circulatory monitoring